## Slide 1: Beginner’s Guide to RTTY Operation
SEMDXA Monthly Meeting
May 8, 2015
Larry Gauthier, K8UT

## Slide 2: Beginner’s Guide to RTTY
Agenda
  Digital Mode Anatomy
        Compare CW to RTTY
  Preparing to Operate RTTY
        Create Your Shopping List
  Connecting the RTTY Components
        Insert Tab A in Slot B
  Operating RTTY Using MMTTY
        Can You Hear Me Now?
  Stuff to Avoid
        Learn from My Mistakes

## Slide 3: CW: The Morse Code - 1836
Morse Code Character Set (42)
  Upper-case characters: A - Z
  Numbers: 0 - 9
  Some punctuation:
      / , . ? – (plus newest @ for email)
  Prosigns:
    Error, Break, End-of-Transmission, End-of-QSO, Wait

## Slide 4: CW: The Morse Code
Morse Code Architecture
  Asynchronous transmission
    No prior agreement on speed
    CW speed is deduced from element times
      Dots = 1 timing element long
      Dashes = 3 timing elements long
      Intra-character spacing = 1 timing element long
      Inter-character spacing = 3 timing elements long
      Inter-word spacing = 6 timing elements long
  Variable character lengths
    Shortest character = E = 1 timing element long
    Longest character = 0 = 19 timing elements long

## Slide 5: CW: The Morse Code
Speed in measured in Words Per Minute (WPM)
  Special word : Paris (50 time elements)
      . _ _ . . _ . _ . . . . . .
  At 60 WPM a dot = 20 milliseconds, a dash = 60 milliseconds
    Formula: timing element length = 1.2/words per minute
Sample CW transmission at 60 WPM
    CQ DE N8SL (8 transmitted characters, sent 3 times)
  _ . _ . _ _ . _ _ . . . _ . _ _ _ . . . . . . _ . .
  C Q D E N 8 S L

## Slide 6: RTTY: The Baudot Code -1870
Baudot Code Character Set (54)
  Upper-case characters: A - Z
  Numbers: 0 - 9
  More punctuation:
      / , . ? – & # ! ‘ “ ( ) : ; <space> <cr> <lf> <bell>
  Control Characters:
    Shift-to-Letters, Shift-to-Figures (more on these later)

## Slide 7: RTTY: The Baudot Code
Baudot Code Architecture
  Pseudo-synchronous transmission
    Requires prior agreement on speed
      All characters are 5 bits long
      All characters are preceded by a start bit (usually 1x)
      All characters are succeeded by a stop bit (usually 1.5x)
      Each character is precisely 7.5 bits long
  RTTY protocol has no error correction
    Many sources of reception errors
      QRM, QRN, fading, multi-path, tropospheric distortion

## Slide 8: RTTY: The Baudot Code
Baudot Character Set (54) ????
How do you get 54 characters from 5 bits?
  Maximum from 5 bits would be 31 characters
Use Shift-Letters and Shift-Figures commands
  Letters = A – Z and <space> <cr> <lf>
  Figures = 0 – 9 and punctuation
    plus <space> <cr> <lf> <bell>
  Strange expressions appear on your screen when the shift commands get garbled in transmission

## Slide 9: RTTY: The Baudot Code
RTTY = Frequency Shift with a Constant Carrier
    Unlike CW with its intermittent carrier
  Frequency shift on Ham Bands = 170 Hz
    Defaults are Mark Hz = 2125, Space Hz = 2295
  Blank time between characters is filled with “diddles”
    Non-printing characters that maintain synchronization
    Results in 100% duty cycle during transmit

## Slide 10: RTTY: The Baudot Code
RTTY Speed is Measured in Baud
  Four FCC approved amateur baud rates:
    45.45 (60wpm), 50 (67wpm), 56 (75 wpm), 75 (100 wpm)
    Most amateur RTTY operation is 45.45 baud (60 wpm)
  At 45.45 baud, bit length is 22.002 milliseconds
  Formula: bit length in milliseconds = 1 / baud rate
Sample RTTY transmission at 45.45 baud
    CQ DE N8SL (12 transmitted characters, sent 3 times)
-01110=-10111=-00100=-01001=-00001=-00100=
C Q space D E space
-01100=-11011=-00110=-11111=-00101=-10010=
N FIGS 8 LTRS S L

## Slide 11: Preparing to Operate RTTY
What do I need to buy?
Popular scenarios:
  RTTY-equipped transceiver
  PC with RTTY software and a transceiver
  PC with RTTY software, a TNC, and a transceiver

## Slide 12: Preparing to Operate RTTY
What do I need to buy?
  RTTY-equipped transceiver
    All you need is the radio, and maybe a keyboard
  PC with RTTY software and a transceiver
    RTTY software (most programs are free)
    Cables between PC and the radio
      Homebrew, commercial cables, commercial interfaces
  PC with RTTY software, a TNC, and a transceiver
    RTTY Software (must have drivers for your TNC)
    A TNC (Terminal Node Controller) or equivalent*
    Cables from PC-to-TNC, TNC-to-Radio

## Slide 13: Connecting the Components
RTTY-equipped transceiver
    RTTY encoder and decoder are built-in
    Can be used with an optional keyboard
  Disadvantages
    Expensive radio
    Minimal functionality (*)
    No log integration
    Limited function keys
    Poor contest exchange
    This is the least popular method
    (easy, expensive, few features)

## Slide 14: Connecting the Components
PC with RTTY software and a transceiver
    Software: MMTTY, fldigi, WinWarbler… others
    Homebrew or commercial interface and cables
    This is the most popular method
    (easy, cheap, full-featured)
Push to Talk (PTT)
AFSK or FSK input
Rx audio out to PC mic In

## Slide 15: Connecting the Components
PC with RTTY software and a transceiver
Options for connecting receive audio
  A microphone plugged into PC mic input
  Direct front/rear panel jack to PC mic/aux input
  Direct but add an audio isolation transformer
  USB cable with audio codecs
  Commercial interfaces
    microHAM, West Mountain Radio, MFJ, others…
Rx audio out to PC mic In

## Slide 16: Connecting the Components
PC with RTTY software and a transceiver
Options for connecting PTT for transmit
  PC serial port DTR/RTS pins to ACC jack Tx line
    Requires simple one resistor, one transistor buffer
  PC USB-to-serial adapter (FTDI chipset recommended)
    Requires simple one resistor, one transistor buffer
  Commercial interface
  *VOX* - if using AFSK. No PTT circuit needed
Push to Talk (PTT)

## Slide 17: Connecting the Components
PC with RTTY software and a transceiver
Options for connecting AFSK transmit
  Direct front panel mic input or rear panel aux jack to PC speaker or Aux audio output
  Direct but add an audio isolation transformer
  USB cable with audio codecs (radios with USB out)
  Commercial interfaces
AFSK input

## Slide 18: Connecting the Components
PC with RTTY software and a transceiver
Options for connecting FSK transmit
  PC serial port Data out pin to ACC jack FSK line
    Requires simple one resistor, one transistor buffer
  PC USB-to-serial adapter (FTDI chipset recommended)
  Commercial interface
FSK input

## Slide 19: Connecting the Components
PC with RTTY software a TNC and a transceiver
Options for connecting a TNC
  Software: MMTTY, fldigi, WinWarbler… others
    Requires driver support for your model TNC
  Serial cable from PC to TNC (serial port or USB)
  Three cables between TNC and transceiver
      (see previous slide)
Push to Talk (PTT)
AFSK or FSK input
Rx audio out to TNC In
Serial or USB
    The middle of the popularity ratings
    (hard, expensive, full-featured)

## Slide 20: Connecting the Components
PC with RTTY software a TNC and a transceiver
Options for connecting “or Equivalent”
  TNC is replaced by Single Board Computer: Arduino
  Software: On PC, MMTTY on N1MM and 2Tone
  Software: On Arduino, tinyFSK (free) by Andy K0SM
    Serial cable from PC to SBC (serial port or USB)
    Two cables between TNC and transceiver
    One audio cable from PC to transceiver
Push to Talk (PTT)
AFSK or FSK input
Rx audio out to PC mic In
Serial to USB
2Tone interface now available!
Raspberry Pi version coming soon!

## Slide 21: Operating RTTY with MMTTY
Operating RTTY Using MMTTY
        Can You Hear Me Now?
  MMTTY as a stand-alone program
    But MMTTY can be used as a slave app beneath many logging programs (N1MM, WinTest, DXLabs, HRD, WinWarbler, DX4Win, …)

## Slide 22: Operating RTTY with MMTTY
MMTTY as a standalone program
Screenshot – the MMTTY application window

## Slide 23: Operating RTTY with MMTTY
Step 1 - MMTTY Go / No-Go Test
  Is receive working?
  Is transmit working?

## Slide 24: MMTTYLaunch.MP4

## Slide 25: Operating RTTY with MMTTY
Step 2 – Tune and Decode a RTTY Signal

## Slide 26: FirstRTTYrcv.mp4

## Slide 27: Operating RTTY with MMTTY
Step 3 – My First QSO
  BUT – before doing that…
    Examine/adjust the Function Key assignments

## Slide 28: Operating RTTY with MMTTY
Step 3 – My First QSO
  BUT – before doing that…
    Examine/adjust the Function Key assignments
      Call CQ CQ CQ DE %m %m PSE K \
      Call CQing station %c %c DE %m %m %m K \
      Send signal report TU UR %r %r DE %m K \
      Start Tx %c DE %m FB %n
      End Tx BTU %n %c DE %m K \
      End QSO 73 %n %c DE %m SK \

## Slide 29: MyFirstQSO.mp4

## Slide 30: Operating RTTY with MMTTY
Learn from My Mistakes
  26,551 RTTY QSOs
  330 DXCC Countries Worked/Confirmed

## Slide 31: Stuff to Avoid
Learn from My Mistakes
  Do not try to decode non-ham RTTY signals
    Non-standard baud and shift, usually encrypted
  Do not operate out-of-band for US stations
    Understand FCC Band Allocations vs ARRL Band Plans
      Post an ARRL RTTY Band Plan map in your shack
      Some WARC bands have narrow (10 KHz!) RTTY plans
    Popular RTTY frequencies – just remember #84
      3.584, 7.034(DX)/7.084(US), 14.084, 21.084, 28.084
  Examine the advantages and disadvantages of AFSK vs FSK operation
    If you choose AFSK, monitor your ALC and audio levels

## Slide 32: Stuff to Avoid
Learn from My Mistakes
  Using AFC is easy, but…
    When using FSK results in RX / TX frequency skew
    With AFSK, can shift frequencies down enough for 2nd harmonics to be in the Tx passband
  Reverse RTTY – “You’re Upside Down”
    Some radios operate RTTY from USB, others from LSB
      Mark/Space = Low/Hi vs Mark/Space = Hi/Low
  Smoke test - power ratings for radio, amp, antenna
    Unlike phone or CW, RTTY is continuous duty Tx

## Slide 33: Stuff to Avoid
Learn from My Mistakes
  Avoid issues with USB-to-serial adapters
    Generally FTDI chipsets are your safest choice
  Recognize shift-LTRS and shift-FIGS problems
    Most likely replacement: adjacent row of keys
    When you see letters and expected numbers, or see numbers and expected letters
    Most common examples
      Signal report: TOO TOO (599 599)
      Contest serial number: PPQ PPQ (001 001)
      You own callsign: K875 K875 (K8UT K8UT)

## Slide 34: Beginner’s Guide to RTTY Operation
The End … almost
Larry Gauthier, K8UT

## Slide 35: K8UTn1mmSO2Vk1n
K8UT’s contest RTTY configuration for SO2V